## Slide 1
Green Corridor for Ambulances
A working simulation of Kuwait City's traffic signals clearing the road ahead of an emergency vehicle — automatically, safely, and back to normal the moment it has passed.
Built on real OpenStreetMap roads of Kuwait City · Eclipse SUMO traffic microsimulation · Presented to the Ministry, August 2026
Notes: Presenter 1 (slides 1–2).
Opening line: 'Every minute an ambulance spends waiting at a red light is a minute taken from a patient. We built a system — and tested it on a faithful model of Kuwait City — where the lights clear the way before the ambulance arrives.'
Keep this slide up for 20 seconds. Do not read the subtitle; say it in your own words.

## Slide 2
The problem: red lights cost ambulances minutes
Today an ambulance with its lights on still meets the same signals as everyone else.
1
Waiting at the red
On a typical downtown run an ambulance meets 8 signals. Each red adds tens of seconds while the patient waits.
2
Nowhere to go
Even when drivers want to give way, a full queue at a red light has no space to move aside.
3
Crossing on red is unsafe
Driving through a red light against live traffic is the most dangerous moment of the whole journey.
Our goal: the signal ahead is already green when the ambulance reaches it — and the traffic in front has already moved.
Kuwait Ambulance Green Corridor · 2 / 8
Notes: Presenter 1.
Three points, one per card: time lost at each red; drivers cannot give way when the queue is stopped; running a red is dangerous.
The '8 signals' figure comes from the system's own dispatch log (e.g. Amiri Hospital to downtown: 4.1 km, 8 signals).
Close with the goal sentence in green — it is the whole project in one line.

## Slide 3
What we built: a living model of Kuwait City's roads
Not a drawing — a simulation where every car, signal and ambulance behaves second by second.
1
Real roads
Downtown Kuwait City is taken directly from OpenStreetMap: one-way streets, turn rules and 78 signalized junctions. A second model covers all six governorates (223 junctions).
2
Real traffic behaviour
Built on Eclipse SUMO, the traffic simulator used by transport authorities worldwide. Demand follows the Kuwaiti weekday pattern, hour by hour — 07:00 peak, near-empty streets at 03:00.
3
Built for people, not engineers
A live map for the control room, a phone screen for the ambulance driver, an operations log for supervisors, and an animated explainer in Arabic and English.
78
signalized junctions, downtown model
223
junctions, six-governorate model
1 hospital
per governorate, real MoH sites
Kuwait Ambulance Green Corridor · 3 / 8
Notes: Presenter 2 (slide 3).
Key message: this is tested on Kuwait's actual street layout, with traffic that rises and falls like a real Kuwaiti weekday.
If asked 'what is SUMO?': an open-source traffic microsimulator from the German Aerospace Center (DLR), the standard research and planning tool for signal studies.
If asked about signal timings: the road layout and signal locations are real; the individual signal timing plans are synthetic until the Ministry provides the real ones (see slide 8).

## Slide 4
How it works: five steps, then back to normal
Every step happens automatically. No one in the ambulance or control room presses a button.
1
Camera sees the lights
A camera at each junction recognises an ambulance with its emergency lights on, up to 200 m away.
›
2
Control centre confirms
The first camera hit confirms the vehicle. The centre already knows its dispatched route, so every junction ahead knows it is coming.
›
3
Green arrives just in time
Each signal switches about 25 seconds before the ambulance reaches it — so the queue in front has time to clear.
›
4
Ambulance passes on green
Conflicting directions wait at red. The ambulance crosses at speed without ever facing a red light.
›
5
Back to normal
Two seconds after it passes, the junction returns to its normal programme. Cross traffic resumes.
Kuwait Ambulance Green Corridor · 4 / 8
Notes: Presenter 3 (slides 4–5).
Walk left to right. The traffic light on each card shows what the ambulance's own signal looks like at that moment.
Important detail in step 3: the switch is based on ARRIVAL TIME (about 25 s ahead), not a fixed distance. If the ambulance is crawling in a jam, junctions far ahead are not held for minutes — that protects cross-street traffic. The window is never earlier than 800 m out and never later than 160 m out.
Step 2: detection confirms, the route predicts — the junction knows before its camera sees.

## Slide 5
Safety first: what the system will never do
A green corridor is only acceptable if it is at least as safe as a normal signal. These rules are built in.
✓
Never a sudden switch
Conflicting traffic always gets 3 seconds of amber, then 2 seconds of all-red, before the corridor turns green. Cars already inside the junction have time to leave.
✓
Never a dark signal
Signals are never switched off. Every junction always shows a proper red, amber or green to every direction.
✓
Never held too long
A single hold is capped at 90 seconds. After that, cross traffic is guaranteed a normal cycle — unless the ambulance is already at the stop line.
✓
Never boxed in
While the ambulance is physically inside the junction, the green is kept. A signal can never return to red with the ambulance halfway across.
Kuwait Ambulance Green Corridor · 5 / 8
Notes: Presenter 3.
This slide answers the question every traffic engineer will ask: 'Is this safe for the other drivers?'
The controller holds a REAL phase of the junction's own programme (the one that serves the ambulance's approach), not an invented 'everything red' state. That is how real preemption controllers work and it keeps compatible movements alive so the junction cannot deadlock.
Numbers: amber 3 s, all-red 2 s, maximum hold 90 s, cooldown for cross traffic 20 s.

## Slide 6
Beyond the green light: the intelligence around it
Six capabilities that turn a signal trick into an operating system for emergencies.
1
Own route planner
The fastest route is computed on live travel times, respecting one-way streets and turn rules. The driver's screen and the signals follow the same route.
2
Scene, then hospital
On arrival the corridor pauses while the patient is loaded, then a new route opens automatically to the nearest hospital by travel time.
3
Learns the traffic
Every road is modelled as a small probability model that learns continuously which streets jam and when — and routes around the predicted jam.
4
Two ambulances, one junction
A published decision matrix rules which ambulance goes first. Unclear cases are referred to a human supervisor with one-click buttons.
5
Speed exemption, audited
With lights on, the ambulance may exceed the limit; every speed camera logs the pass as 'NO CITATION' so nothing is left to dispute.
6
Ask the record
Supervisors ask questions in plain language — 'what happened on case A-012?' — and get an answer with citations from the operations log.
Kuwait Ambulance Green Corridor · 6 / 8
Notes: Presenter 4 (slide 6).
Do not go deep on any one item; give one sentence each. The point is that this is a complete operating picture, not only a signal controller.
If asked 'learns the traffic': it is a Markov model (discrete and continuous time) per road, verified against closed-form solutions, and it persists between sessions.
If asked about the supervisor referral: the system decides routine cases itself; only genuinely conflicting priorities go to a person, and every ruling is logged.

## Slide 7
What we measured
Same streets, same traffic, same dispatches — with the green corridor and without it.
Chart: Average ambulance arrival time — 33 logged missions
| Without green corridor | With green corridor
Arrival time (seconds) | 430 | 348
19% faster
mission log, 33 runs
About 80 seconds saved on an average run; the ambulance never stops at a signal.
+9.1% speed
measured at peak demand
Mean speed of all traffic rose when junctions also give early green to a lone waiting approach.
−42.5% halted
measured at peak demand
Fewer vehicles stopped network-wide — other road users gain too, not only the ambulance.
'Without' times are the system's own per-junction estimate of the signal waits the corridor removed, in the same traffic.
Kuwait Ambulance Green Corridor · 7 / 8
Notes: Presenter 5 (slides 7–8).
Read the chart plainly: 430 seconds without, 348 seconds with — about 19% faster, roughly 80 seconds per run, averaged over the 33 missions in the operations log.
Be honest about the method if asked: the 'with' time is measured in the simulation; the 'without' time is the system's own counterfactual estimate of signal waits removed (r²/2C timer formula per junction, same traffic). A seeded side-by-side comparison harness also exists (run_headless.py --compare).
The +9.1% / −42.5% figures are from the demand-responsive signal feature (v2.4), measured at identical peak demand.

## Slide 8
Where we go from here
The model is ready. Three things from the Ministry would turn it into a pilot.
1
Real signal timings
The road layout is real; the signal plans are still synthetic. With the actual timing plans, results become a forecast for specific junctions.
2
Real traffic counts
A small file of hourly counts (hour, multiplier) plugs straight into the model and replaces the calibrated profile.
3
One pilot corridor
Pick a single hospital-to-area corridor. We simulate it first, then it can be tried on the street with the existing camera and controller infrastructure.
Everything shown today runs on an ordinary computer, with no internet connection, and logs every decision for after-action review.
Thank you. Questions welcome.
Notes: Presenter 5.
End on the three asks — these are concrete and cheap for the Ministry to provide.
Closing line: 'We are not asking for a new network of cameras or controllers. We are asking for the data that lets the lights we already have give way to the people who need it most.'
Then open the floor.